## Slide 1: Public engagement activity
Amaan Mujawar
Notes: Good afternoon, my name is Amaan Mujawar, and today I will be presenting my project on Implementing an Arithmetic Unit Utilizing Approximae Computing into a RISC-V SoC.

## Slide 2: ABOUT the project
Implement an Arithmetic Unit Utilizing Approximate Computing into RISC-V SoC.
Supervisor: Mr. Neil Powell
2
Notes: This work is supervised by Mr. Neil Powell at The University of Sheffield.

## Slide 3: Background & motivation
Context
challenge
opportunity
importance
Growing demand for high-performance computing in machine learning, computer vision, and multimedia processing.
Traditional computing approaches are limited by the slowing of Moore's Law.
Approximate computing allows controlled errors for faster and energy-efficient computation.
Enables energy-efficient digital systems, suitable for error-tolerant applications like image processing.
Notes: We live in an era where high-performance computing is essential for applications like machine learning, computer vision, and multimedia processing. However, traditional computing approaches are facing limitations due to the slowing down of Moore’s Law, making it increasingly difficult to achieve significant improvements in speed and efficiency.
To address this, we turn to Approximate Computing—a technique that allows controlled errors in calculations, in exchange for higher energy efficiency and faster processing. This is especially useful for error-tolerant applications such as image processing and AI, where perfect accuracy is not always necessary.

## Slide 4: ARCHITECTURE
8-bit Approximate MAC Unit
Input Fetch Stage
8-bit operands (A and B) for multiplication
Inputs are passed into the fuzzy memoization block to check for stored approximate results
Fuzzy Memoization Block
Caches previous computations to avoid redundant calculations
Uses Hamming distance to find a similar previously stored input-output pair.
If a match is found, cached result is used instead of recalculating.
Approximate Multiplication Stage
Lower-Part OR-based Approximate Multiplier:
  MSB (Most Significant Bits) handled with a Dadda Multiplier
  LSB (Least Significant Bits) approximated using OR-based logic
Partial Product Reduction Stage
Uses compressor-based approximate multipliers
Approximate Addition Stage
Accumulation performed using Lower-Part OR-based Approximate Adders
Notes: At the heart of this project is an 8-bit Approximate Multiply-Accumulate (MAC) Unit, which is designed to improve computational efficiency while reducing power consumption.
The architecture consists of several key components:
Input Fetch Stage: Takes in 8-bit operands and prepares them for computation.
Fuzzy Memoization Block: Caches and reuses previously computed results to minimize redundant operations.
Approximate Multiplication Stage:
  MSBs (Most Significant Bits): Processed using a Dadda Multiplier for accuracy.
  LSBs (Least Significant Bits): Processed using OR-based logic, reducing power consumption.
Partial Product Reduction Stage: Uses compressor-based approximate multipliers for efficiency.
Approximate Addition Stage: Uses Lower-Part OR-based Approximate Adders to accumulate results efficiently.
This architecture enables us to trade off accuracy for improved speed and reduced power consumption, making it well-suited for low-power embedded systems.

## Slide 5: Real-World Problem Addressed
Energy-Efficiency
Traditional computation
Approximate computing
Ideal tasks
Reduced power consumption by allowing controlled errors
Lower energy requirements make it suitable for battery-powered devices
Precise arithmetic units consume more power and area
High accuracy but less energy-efficient
Trades off accuracy for efficiency, reducing power and area
Suitable for error-tolerant applications like image processing and AI
Image processing (denoising, compression)
Machine learning
Signal processing in embedded systems
5
Notes: Why does this matter? Let’s compare traditional computing with approximate computing:
Traditional computation prioritizes precision but at the cost of higher power consumption and larger chip area.
Approximate computing, on the other hand, trades off some accuracy in exchange for significant energy savings and faster processing.
This makes it ideal for applications such as: Image processing (denoising, compression) Machine learning Signal processing in embedded systems
By leveraging approximate computing, this project contributes to the development of energy-efficient digital systems for future computing technologies.

## Slide 6: Aims & Objectives
AIMS
Design and implement an 8-bit Multiply-Accumulate (MAC) unit using approximate computing techniques
Implement an arithmetic unit utilizing approximate computing into a RISC-V SoC
Optimize the arithmetic unit for energy efficiency while maintaining acceptable computational accuracy.
OBJECTIVES
Design and simulate the MAC unit using Verilog on FPGA
Integrate the MAC unit into a RISC-V SoC
Evaluate, analyze and compare performance, power consumption, and accuracy against traditional designs
Validate the design using simulation tools
Assess the impact of approximation on computational accuracy
Evaluate the MAC unit’s performance in a fuzzy memoized FIR filter for image processing
Notes: The primary aim of this project is to design and implement an 8-bit MAC unit using approximate computing techniques and integrate it into a RISC-V SoC. To achieve this, we set the following objectives: - Design and simulate the MAC unit using Verilog on FPGA - Integrate the MAC unit into a RISC-V SoC - Evaluate power consumption, accuracy, and speed - Validate the design through unit testing and FPGA simulations
This structured approach ensures that we can balance accuracy, power consumption, and computational speed effectively.

## Slide 7: Problem specification
Problem:
Balancing accuracy, power consumption, and speed in arithmetic units
Expected Results:
Enhanced computational efficiency with minimal accuracy loss
Reduced power consumption and chip area
Methodology:
Using Verilog for implementation and FPGA simulations
Implementing Approximate Adders and Approximate Multipliers based on existing designs
Notes: The key challenge in this project is achieving a balance between accuracy, power, and speed.
To address this, we implemented: Approximate Adders and Multipliers based on existing research Verilog for implementation and FPGA-based simulations Performance evaluations to compare with traditional MAC units
The expected outcome is a highly efficient arithmetic unit that minimizes power consumption while maintaining acceptable accuracy levels.

## Slide 8: SIMULATION RESULTS - ADDER
8

## Slide 9: SIMULATION RESULTS - Multiplier
9

## Slide 10: Analysis and Significance
10

## Slide 11: UNIT TESTING - Adder
11

## Slide 12: UNIT TESTING - Multiplier
12

## Slide 13: Comparison: Aims and milestones
Achievements
Pending Tasks
Established a benchmark with a pipelined MAC unit
Conceptual and partial implementation of AAUD architecture
Implemented Approximate Adder and Approximate Multiplier
Unit testing completed and modules validated
Complete integration of approximate multipliers and adders
Explore Fuzzy memoization implementation
Conduct comprehensive testing for power, speed, and accuracy
Compare against other approximation units to evaluate performance
Notes: So far, the project has achieved: Benchmarking of a pipelined MAC unit Implementation of Approximate Adders and Multipliers Unit testing and validation of individual modules
However, pending tasks include: Full integration of approximate components Exploring Fuzzy Memoization for further optimizations Conducting comprehensive testing for power, speed, and accuracy

## Slide 14: Future Work Plan
Next steps
Complete implementation of approximate arithmetic units
Integrate AAUD into RISC-V SoC and conduct full system testing
Evaluate performance against traditional MAC units
Long-term
Explore further optimizations with different approximation methods
Investigate potential applications in other error-tolerant domains, such as machine learning
Notes: Moving forward, the next steps will be: - Completing the integration of approximate arithmetic units - Embedding the MAC unit into a RISC-V SoC for full system testing - Comparing performance against traditional MAC units
In the long-term, we aim to: - Explore further optimizations with different approximation methods - Investigate applications in other error-tolerant domains such as AI and machine learning

## Slide 16: THANK YOU
Amaan Mujawar​
aurmujawar1@sheffield.ac.uk
The University of Sheffield – Electronics and Computer Engineering
Notes: To summarize, this project demonstrates how Approximate Computing can be leveraged to build energy-efficient, high-performance arithmetic units. By designing an 8-bit Approximate MAC Unit and integrating it into RISC-V SoC, we take a step toward addressing modern computational challenges in a power-efficient and scalable manner.
Thank you all for your time and attention. I would be happy to take any questions.