## Slide 1: Public engagement activity
Amaan Mujawar
● who may not be familiar with the specific details behind your project.
●What is given, and what are the expected results? What methodology are you using?
● Technical progress achieved so far, preliminary experimental/simulation/theoretical
results, along with your analysis of them. Significance of the results achieved.
● Comparison against aims and objectives, and future work plan milestones

## Slide 2: ABOUT the project
Implement an Arithmetic Unit Utilizing Approximate Computing into RISC-V SoC.
Supervisor: Mr. Neil Powell
Notes: Hello, My name is Amaan Mujawar, and today I’ll be presenting my project titled "Implement an Arithmetic Unit Utilizing Approximate Computing into RISC-V SoC." This project is supervised by Mr. Neil Powell and is part of my work at the University of Sheffield in the Department of Electronics and Electrical Engineering. I’ll be discussing the background, motivation, progress, and future directions of this project.

## Slide 3: Background & motivation
Context
challenge
opportunity
importance
Growing demand for high-performance computing in machine learning, computer vision, and multimedia processing.
Traditional computing approaches are limited by the slowing of Moore's Law.
Approximate computing allows controlled errors for faster and energy-efficient computation.
Enables energy-efficient digital systems, suitable for error-tolerant applications like image processing.
Notes: Approximate computing is an emerging technique that allows a small degree of error in computations to reduce power consumption and execution time. This approach is especially relevant today as the demand for high-performance computing grows rapidly in fields like machine learning, computer vision, and multimedia processing. However, traditional methods are limited by the slowing of Moore's Law, which states that the number of transistors on a chip doubles every two years. As this trend slows, new approaches are needed to achieve performance and energy efficiency gains. Approximate computing offers a solution by introducing controlled errors in non-critical computations, making it ideal for error-tolerant applications like image processing.

## Slide 4: ARCHITECTURE
Notes: This project specifically addresses the challenge of balancing accuracy, power consumption, and speed in arithmetic units. In this context, we’re using the Nexys-A7 FPGA and Xilinx Vivado Design Suite for simulations and testing. The goal is to achieve enhanced computational efficiency while maintaining minimal accuracy loss. To do this, we are implementing three key techniques:
Lower-Part OR-based Approximate Multipliers for faster partial product calculations.
Approximate Adders to accumulate results efficiently.
Fuzzy Memoization to cache and reuse results in repetitive calculations, reducing redundant computations. Together, these techniques form a powerful combination for building efficient, error-tolerant arithmetic units.

## Slide 5: Real-World Problem Addressed
Energy-Efficiency
Traditional computation
Approximate computing
Ideal tasks
Reduced power consumption by allowing controlled errors
Lower energy requirements make it suitable for battery-powered devices
Precise arithmetic units consume more power and area
High accuracy but less energy-efficient
Trades off accuracy for efficiency, reducing power and area
Suitable for error-tolerant applications like image processing and AI
Image processing (denoising, compression)
Machine learning
Signal processing in embedded systems
Notes: One of the biggest challenges in modern computing is balancing performance with power consumption. Traditional precise computation methods require significant power and resources, making them less efficient for data-intensive tasks. Approximate computing addresses this by allowing minor inaccuracies, leading to faster computations with lower power consumption. This makes it especially useful for tasks where perfect accuracy is not necessary, like image and video processing, where slight inaccuracies are imperceptible to the human eye. By leveraging this, the project aims to design a highly efficient arithmetic unit for a RISC-V System on Chip.

## Slide 6: Aims & Objectives
AIMS
Design and implement an 8-bit Multiply-Accumulate (MAC) unit using approximate computing techniques
Implement an arithmetic unit utilizing approximate computing into a RISC-V SoC
Optimize the arithmetic unit for energy efficiency while maintaining acceptable computational accuracy.
OBJECTIVES
Design and simulate the MAC unit using Verilog on FPGA
Integrate the MAC unit into a RISC-V SoC
Evaluate, analyze and compare performance, power consumption, and accuracy against traditional designs
Validate the design using simulation tools
Assess the impact of approximation on computational accuracy
Evaluate the MAC unit’s performance in a fuzzy memoized FIR filter for image processing
Notes: The primary aim of this project is to design and implement a 32-bit Multiply-Accumulate (MAC) unit using approximate computing techniques for integration into a RISC-V SoC. To achieve this, the project follows several specific objectives:
Conduct a comprehensive literature review to select suitable approximation methods.
Design and simulate the MAC unit using Verilog and test it on FPGA hardware.
Integrate the MAC unit into the RISC-V SoC framework, ensuring compatibility and functionality.
Finally, evaluate its performance, power consumption, and accuracy against traditional designs to measure the trade-off between efficiency and precision.

## Slide 7: SPECIFICATION
Notes: This project specifically addresses the challenge of balancing accuracy, power consumption, and speed in arithmetic units. In this context, we’re using the Nexys-A7 FPGA and Xilinx Vivado Design Suite for simulations and testing. The goal is to achieve enhanced computational efficiency while maintaining minimal accuracy loss. To do this, we are implementing three key techniques:
Lower-Part OR-based Approximate Multipliers for faster partial product calculations.
Approximate Adders to accumulate results efficiently.
Fuzzy Memoization to cache and reuse results in repetitive calculations, reducing redundant computations. Together, these techniques form a powerful combination for building efficient, error-tolerant arithmetic units.

## Slide 8: Problem specification
Problem:
Balancing accuracy, power consumption, and speed in arithmetic units
Expected Results:
Enhanced computational efficiency with minimal accuracy loss
Reduced power consumption and chip area
Methodology:
Using Verilog for implementation and FPGA simulations
Implementing Approximate Adders and Approximate Multipliers
Notes: This project specifically addresses the challenge of balancing accuracy, power consumption, and speed in arithmetic units. In this context, we’re using the Nexys-A7 FPGA and Xilinx Vivado Design Suite for simulations and testing. The goal is to achieve enhanced computational efficiency while maintaining minimal accuracy loss. To do this, we are implementing three key techniques:
Lower-Part OR-based Approximate Multipliers for faster partial product calculations.
Approximate Adders to accumulate results efficiently.
Fuzzy Memoization to cache and reuse results in repetitive calculations, reducing redundant computations. Together, these techniques form a powerful combination for building efficient, error-tolerant arithmetic units.

## Slide 9: SIMULATION RESULTS
Notes: So far, significant technical progress has been made. We began by implementing and testing a pipelined MAC unit on FPGA, which serves as a benchmark to measure the improvements made by the approximate designs. Following this, the conceptual design of the Approximate Arithmetic Unit Design (AAUD) was completed, and initial implementation of approximate multipliers and adders is underway. Preliminary results show that the pipelined MAC unit achieves promising throughput and power efficiency. However, we are continuously refining the design to fully integrate the approximation techniques for better performance.

## Slide 10: Analysis and Significance
Performance Analysis
✅ Power Efficiency – Reduces power using OR-based adders & compressor-based multipliers. ✅ Area Reduction – Lower transistor count, optimized for FPGA/SoC. ✅ Speed & Latency – Pipelining improves throughput, approximation speeds computation. ✅ Accuracy Trade-off – Small errors measured using MRED; acceptable for image processing.
2️⃣ Why is this Significant?
🔹 Overcomes Moore’s Law Limitations – Alternative efficiency technique for post-scaling era. 🔹 Optimized for Edge Computing & IoT – Low-power design fits embedded applications. 🔹 Application in Image Processing – Used in fuzzy memoized FIR filters for denoising. 🔹 Future Potential – Scalable to 16-bit, 32-bit MACs; applicable in AI & DSP.
Notes: So far, significant technical progress has been made. We began by implementing and testing a pipelined MAC unit on FPGA, which serves as a benchmark to measure the improvements made by the approximate designs. Following this, the conceptual design of the Approximate Arithmetic Unit Design (AAUD) was completed, and initial implementation of approximate multipliers and adders is underway. Preliminary results show that the pipelined MAC unit achieves promising throughput and power efficiency. However, we are continuously refining the design to fully integrate the approximation techniques for better performance.

## Slide 11: UNIT TESTING - Adder
Notes: So far, significant technical progress has been made. We began by implementing and testing a pipelined MAC unit on FPGA, which serves as a benchmark to measure the improvements made by the approximate designs. Following this, the conceptual design of the Approximate Arithmetic Unit Design (AAUD) was completed, and initial implementation of approximate multipliers and adders is underway. Preliminary results show that the pipelined MAC unit achieves promising throughput and power efficiency. However, we are continuously refining the design to fully integrate the approximation techniques for better performance.

## Slide 12: UNIT TESTING - Multiplier
Notes: So far, significant technical progress has been made. We began by implementing and testing a pipelined MAC unit on FPGA, which serves as a benchmark to measure the improvements made by the approximate designs. Following this, the conceptual design of the Approximate Arithmetic Unit Design (AAUD) was completed, and initial implementation of approximate multipliers and adders is underway. Preliminary results show that the pipelined MAC unit achieves promising throughput and power efficiency. However, we are continuously refining the design to fully integrate the approximation techniques for better performance.

## Slide 13: Comparison Against Aims and Objectives
Achievements
Pending Tasks
Established a benchmark with a pipelined MAC unit
Conceptual and partial implementation of AAUD architecture
I
Complete integration of approximate multipliers and adders.
Conduct comprehensive testing for power, speed, and accuracy.
Notes: The key finding so far is the trade-off between accuracy and efficiency. By introducing controlled errors, we can significantly reduce power consumption and increase speed. Fuzzy memoization, in particular, has shown great potential in reducing redundant calculations in image processing tasks. The significance of this project lies in its ability to create scalable, energy-efficient arithmetic units. It provides a solution to the limitations of traditional computing scaling methods and paves the way for more efficient digital systems.

## Slide 14: Future Work Plan
Next steps
Complete implementation of approximate arithmetic units
Integrate AAUD into RISC-V SoC and conduct full system testing
Evaluate performance against traditional MAC units
Long-term
Explore further optimizations with different approximation methods
Investigate potential applications in other error-tolerant domains, such as machine learning
Notes: Comparing the progress against the initial aims and objectives: We have successfully established a benchmark with the pipelined MAC unit and completed the conceptual design of the AAUD. Partial implementation of approximate multipliers and adders is ongoing, and initial results are promising. However, we still need to complete the integration of all approximation techniques and conduct comprehensive testing for power, speed, and accuracy. This comparison helps us identify gaps and guides our next steps to achieve the project’s full potential.

## Slide 15
Notes: The primary aim of this project is to design and implement a 32-bit Multiply-Accumulate (MAC) unit using approximate computing techniques for integration into a RISC-V SoC. To achieve this, the project follows several specific objectives:
Conduct a comprehensive literature review to select suitable approximation methods.
Design and simulate the MAC unit using Verilog and test it on FPGA hardware.
Integrate the MAC unit into the RISC-V SoC framework, ensuring compatibility and functionality.
Finally, evaluate its performance, power consumption, and accuracy against traditional designs to measure the trade-off between efficiency and precision.

## Slide 16: Conclusion
Notes: Looking ahead, the next steps involve completing the implementation of all approximate arithmetic units and integrating them into the RISC-V SoC. Once integrated, extensive testing will be conducted to evaluate power consumption, processing speed, and accuracy. The results will then be compared to traditional MAC units to assess the trade-offs made by using approximate computing. In the long term, this project aims to explore additional approximation methods for further optimizations. There is also potential to expand this approach to other error-tolerant domains, such as machine learning and data analytics.

## Slide 17: THANK YOU
Amaan Mujawar​
aurmujawar1@sheffield.ac.uk
The University of Sheffield – Electronics and Computer Engineering
Notes: In conclusion, approximate computing offers a strategic solution to the growing demands for high-performance and energy-efficient computing. By allowing controlled inaccuracies, it balances efficiency with acceptable error rates, making it ideal for error-tolerant applications like image processing. This project demonstrates the potential of integrating approximate arithmetic units into RISC-V SoC, significantly improving performance and power efficiency. Moving forward, the successful implementation and testing of this design could pave the way for a new generation of energy-efficient digital systems.