## Slide 1: Symposium
Amaan Mujawar
Notes: Good afternoon, my name is Amaan Mujawar, and today I will be presenting my project on Implementing an Arithmetic Unit Utilizing Approximate Computing into a RISC-V SoC.

## Slide 2: ABOUT the project
Design of an Approximate 8-bit MAC Unit: A Step Towards RISC-V SoC Integration
Supervisor: Mr. Neil Powell
2
Notes: This work is supervised by Mr. Neil Powell at The University of Sheffield.

## Slide 3: Background & motivation
Context
challenge
opportunity
importance
Growing demand for high-performance computing in machine learning, computer vision, and multimedia processing.
Traditional computing approaches are limited by the slowing of Moore's Law.
Approximate computing allows controlled errors for faster and energy-efficient computation.
Enables energy-efficient digital systems, suitable for error-tolerant applications like image processing.
Notes: We live in an era where high-performance computing is essential for applications like machine learning, computer vision, and multimedia processing. However, traditional computing approaches are facing limitations due to the slowing down of Moore’s Law, making it increasingly difficult to achieve significant improvements in speed and efficiency.
To address this, we turn to Approximate Computing—a technique that allows controlled errors in calculations, in exchange for higher energy efficiency and faster processing. This is especially useful for error-tolerant applications such as image processing and AI, where perfect accuracy is not always necessary.

## Slide 4: Real-World Problem Addressed
Big Data/Real-Time Processing
High-Performance Computing
Fault Tolerance
Ideal tasks
Improves scalability
Processing speed for real-time data streams (e.g., social media, sensor networks)
Speeds up resource-intensive simulations
Data processing, trading some precision for faster performance and lower power usage.
Improves system reliability by allowing for approximate results during faults or hardware failures
Image processing
Machine learning
Signal processing in embedded systems
4
Notes: Why does this matter? Let’s compare traditional computing with approximate computing:
Traditional computation prioritizes precision but at the cost of higher power consumption and larger chip area.
Approximate computing, on the other hand, trades off some accuracy in exchange for significant energy savings and faster processing.
This makes it ideal for applications such as: Image processing (denoising, compression) Machine learning Signal processing in embedded systems
By leveraging approximate computing, this project contributes to the development of energy-efficient digital systems for future computing technologies.

## Slide 5: Aims & Objectives
AIMS & OBJECTIVES
Design and implement an 8-bit Multiply-Accumulate (MAC) unit using approximate computing techniques
Optimise the arithmetic unit for energy efficiency while maintaining acceptable computational accuracy.
Assess integrability of the arithmetic unit utilising approximate computing into a RISC-V SoC
Design and simulate the MAC unit using Verilog on FPGA
Evaluate, analyze and compare performance, power consumption, and accuracy against traditional designs
Assess the impact of approximation on computational accuracy
Notes: The primary aim of this project is to design and implement an 8-bit MAC unit using approximate computing techniques and integrate it into a RISC-V SoC. To achieve this, we set the following objectives: - Design and simulate the MAC unit using Verilog on FPGA - Validate the design through unit testing and FPGA simulations
- Evaluate power consumption, accuracy, and speed
- Integrate the MAC unit into a RISC-V SoC

## Slide 6: ARCHITECTURE
8-bit Approximate MAC Unit
Input Fetch Stage
8-bit operands (A and B)
Inputs are passed into the fuzzy memoization block to check for stored approximate results
Fuzzy Memoization Block
Caches previous computations to avoid redundant calculations
Instead of storing the exact result for an exact input we store results for approximate matches.
If a match is found, cached result is used instead of recalculating.
Approximate Multiplication Stage
Lower-Part OR-based Approximate Multiplier:
  MSB (Most Significant Bits) handled with a Dadda Multiplier
  LSB (Least Significant Bits) approximated using OR-based logic
Partial Product Reduction Stage
Uses compressor-based approximate multipliers
Approximate Addition Stage
Accumulation performed using Lower-Part OR-based Approximate Adders
Notes: At the heart of this project is an 8-bit Approximate Multiply-Accumulate (MAC) Unit, which is designed to improve computational efficiency while reducing power consumption.
The architecture consists of several key components:
Input Fetch Stage
Fuzzy Memoization Block
Approximate Multiplication Stage:
  MSBs (Most Significant Bits
  LSBs (Least Significant Bits)
  4. Partial Product Reduction Stage:
  5. Approximate Addition Stage:

## Slide 7: What has been achieved
Achievements
Established a benchmark with a pipelined MAC unit
Implemented Approximate Adder and Approximate Multiplier
Unit testing completed and modules validated
Implemented Fuzzy memoization cache look up
Researched on implementing onto RISC-V SoC
Notes: So far, the project has achieved: Benchmarking of a pipelined MAC unit Implementation of Approximate Adders and Multipliers Unit testing and validation of individual modules

## Slide 8: SIMULATION RESULTS - ADDER
8

## Slide 9: SIMULATION RESULTS - Multiplier
9

## Slide 10: THANK YOU
Amaan Mujawar​
aurmujawar1@sheffield.ac.uk
The University of Sheffield – Electronics and Computer Engineering